## Slide 1: STM32 – DIST.
Micro101

## Slide 2: Tools Overview
Overview Portfolio
Evaluation Boards
Free IDEs
  AC6
  CoIDE
  Keil (M0/M0+)
  mbed
Ecosystem
  STM32CubeMX
  STLink Utility
  ST Visual Programmer (STVP)
  STM32 Flash Loader Demonstrator
  Dfuse
  STM Studio

## Slide 3: ST has licensed all Cortex®-M cores
Forget traditional 8/16/32-bit classifications and get
  Seamless architecture across all applications
  Every product optimized for ultra-low power and ease of use
MCU
Binary and tool compatible
Cortex-M0/M0+
Cortex-M3
Cortex-M4
8/16-bit applications
16/32-bit applications
16/32-bit DSC applications
Cortex-M7
16/32-bit DSC applications
Notes: ST is a leading partner with ARM for Cortex-M cores, participating in the definition of these cores. Today, the STM32 portfolio includes [CLICK] the full panel of Cortex-M cores, from the Cortex-M0 and Cortex-M3 to the Cortex-M4. The portfolio offers more than 300 devices in full production.

## Slide 4
STM32 pin-to-pin compatibility(ex: LQFP64 )
Ultra-low-power
Mainstream
CortexTM-M0/0+
Performance
Energy Efficiency
CortexTM-M3
CortexTM-M4
Over 550 pin-to-pin compatible devices

## Slide 5: Broad Range of Development Tools
STM32 Nucleo expansion boards
From full evaluation to open hardware
Flexible prototyping
Key feature prototyping
Full feature evaluation
STM32 Nucleo
Discovery kits
Evaluation boards
3rd parties
www.st.com/stm32nucleo
www.st.com/stm32discovery
Specialized functionality add-on
www.st.com/x-nucleo
Connectivity, Sensors…
Notes: Various types of development boards enable you to get started with the STM32 microcontrollers.
* The STM32 Nucleo boards provide an affordable and flexible way for anyone to try out new ideas and build prototypes with a wide choice of specialized expansion boards.
* The Discovery kits enable users to seamlessly exercise key features of STM32 products, while the Evaluation board exposes all MCU functionalities.
All these development boards include an integrated debugger/programmer as well as a comprehensive software library with examples that help developers to take davantage of STM32 capabilities.

## Slide 6
STM32 ODE
STM32 X-Nucleo Portfolio
Part Number | Marketing Status | Core Product | General Description
P-NUCLEO-6180X1 | Active | VL6180X | VL6180X Nucleo pack - NEW - Includes VL6180X Expansion board and STM32F401RE Nucleo
P-NUCLEO-6180X2 | Active | VL6180X | VL6180X Nucleo pack - NEW - Includes VL6180X Expansion board and STM32L053R8 Nucleo
X-NUCLEO-6180XA1 | Active | VL6180X | Proximity and ambient light sensor expansion board based on VL6180X for STM32 Nucleo
X-NUCLEO-CCA02M1 | Active | MP34DT01-M | Digital MEMS microphones expansion board based on MP34DT01-M for STM32 Nucleo
X-NUCLEO-IKS01A1 | Active | LSM6DS0; LIS3MDL; LPS25HB; HTS221 | Motion MEMS and environmental sensor expansion board for STM32 Nucleo
Sensors Expansion Boards
Proximity
Motion MEMS
Environmental Sensors
MEMS Microphones

## Slide 7
STM32 ODE
STM32 X-Nucleo Portfolio
Connectivity Expansion Boards
Bluetooth Smart
SubGhz
NFC
Part Number | Marketing Status | Core Product | General Description
X-NUCLEO-IDB04A1 | Active | BlueNRG; BALF-NRG-01D3 | Bluetooth low energy expansion board based on BlueNRG for STM32 Nucleo
X-NUCLEO-IDB05A1 | Evaluation | SPBTLE-RF;BlueNRG-MS;BALF-NRG-01D3 | Bluetooth Low Energy expansion board based on SPBTLE-RF module for STM32 Nucleo
X-NUCLEO-IDS01A4 | Active | SPSGRF-868 | Sub-1 GHz RF expansion board based on the SPSGRF-868 module for STM32 Nucleo
X-NUCLEO-IDS01A5 | Active | SPSGRF-915 | Sub-1 GHz RF expansion board based on the SPSGRF-915 module for STM32 Nucleo
X-NUCLEO-NFC01A1 | Active | M24SR64-YMN6T/2 | Dynamic NFC tag expansion board based on M24SR for STM32 Nucleo

## Slide 8
STM32 ODE
STM32 X-Nucleo Portfolio
Motor Control Expansion Boards
Stepper Motors
Brush DC
NFC
Part Number | Marketing Status | Core Product | General Description
X-NUCLEO-IHM01A1 | Active | L6474PD | Stepper motor driver expansion board based on L6474 for STM32 Nucleo
X-NUCLEO-IHM03A1 | Active | powerSTEP01 | High power stepper motor driver expansion board based on powerSTEP01 for STM32 Nucleo
X-NUCLEO-IHM04A1 | Active | L6206 | Dual brush DC motor driver expansion board based on L6206 for STM32 Nucleo
X-NUCLEO-IHM05A1 | Active | L6208 | Bipolar stepper motor driver expansion board based on L6208 for STM32 Nucleo
Part Number | Marketing Status | Core Product | General Description
X-NUCLEO-PLC01A1 | Active | CLT01-38SQ7;VNI8200XP | Industrial input/output expansion board based on VNI8200XP and CLT01-38SQ7 for STM32 Nucleo
Input-Output Expansion Boards

## Slide 9: Comprehensive choice of IDEs
Monitor
Generate Code
Compile & Debug
STM32CubeMX
Partners IDEs
STMStudio
Free IDE

## Slide 10: System Workbench for STM32
Free Eclipse-based flexible software development environment :
  Covers the full range of STM32 mcus and associated boards (Nucleo, Discovery, Eval).
  Comprehensive support for STM32 firmware (Standard Peripheral library or Cube HAL).
  Customisation enabled through Eclipse plug-ins (SVN, EGit…).
Key features :
  GCC C/C++ compiler.
  GDB-based debugger.
  ST-Link support.
  Multi-OS support : Windows, Linux & OSX (Q2’2015).
  No code size limit.
  SW4STM32 project format will be supported by CubeMX.

## Slide 11: System Workbench for STM32
How to download SW4STM32 ?
  Go to associated collaborative site at www.openstm32.org
  Register to this site.
  Get installation instructions at the Documentation > System Workbench page.
  Proceed with immediate download of the toolchain.
Technical support :
  Handled through the associated Openstm32 website.
  Documentation, forum, blog, trainings are available to provide assistance to users.

## Slide 12: CoIDE
Free Eclipse-based simplified software development environment:
  Supports all STM32 mcus and Nucleo boards.
  Supports STM32Cube firmware (HAL).
  Download and Technical support available through collaborative site at www.coocox.org
Key features :
  GCC C/C++ compiler.
  GDB-based debugger.
  No code size limit.
  ST-Link support.
  English and Chinese languages are supported.

## Slide 13: MDK-ARM
Comprehensive software development environment for Cortex-M devices :
  Free version for ST supports all STM32F0 and STM32L0 mcus and associated boards (Nucleo, Discovery, Eval).
  Comprehensive support for STM32 firmware (Std Peripheral library or Cube HAL).
  Technical support available through the ARM Connected Community site at community.arm.com
Key features :
  ARM C/C++ compiler.
  uVision IDE, debugger and simulation environment.
  CMSIS-compliant.
  ST-Link support.
  English, Chinese, Japanese, Korean languages are supported.
  The setup of peripherals configured by CubeMX is directly exported to MDK.

## Slide 14: Free MDK-ARM for ST
Free licenses for STM32 devices based on Cortex-M0/M0+ cores :
  Applicable immediately to all STM32F0 and STM32L0 mcus.
  PC-locked multi-year licenses.
  No code size limit.
  Multiple language support.
  Technical support included.
Direct download from Keil website :
  No limit of number of downloads by customer.
  Direct access to configuration files for STM32 and associated boards.
  Free access to MDK-ARM periodic updates.
How to get free MDK-ARM licenses for STM32F0 and STM32L0 ?
  Go to Keil website at : www.keil.com/mdk-st
  Download MDK-ARM toolchain.
  Activate the free license using this Product Serial Number (PSN) : U1E21-CM9GY-L3G4L

## Slide 15: Comprehensive choice of STM32 free IDEs
Q2’2015
Q2’2015
Free licenses for all STM32 microcontrollers
Free licenses for STM32F0 & STM32L0
Free access to all STM32Nucleo users
System Workbench
CoIDE
MDK-ARM

## Slide 16: STM32 Embedded Software Offer - Overview
ST Offering. Free
Partners Offer
Abstraction Level
Portability Level
STM32Snippets
Standard Peripheral Libraries
STM32Cube
Mbed Core
« C » partners
Micrium, SEGGER,
HCC, ….
Virtual Machines
With partners
.Net, Java
IS2T, Oracle, Mountainer, .…
STM32 Device
-specific
f.i.: STM32F072
STM32 Series
-specific
f.i.: STM32F1
STM32 Family
-specific
Cortex-M based
MCUs
-specific
Any MCU
Beyond MCU
world

## Slide 17: STM32Snippets
What is it ?
  A collection of code examples, directly based on STM32 peripheral registers, available in documentation and as software bundles
Target Audience
  low level embedded system developers, typically coming from an 8 bit background, used to assembly or C with little abstraction
Portability | Optimization (Memory & Mips) | Easy | Readiness | Hardware coverage
 | +++ |  |  | +
Features:
  Highly Optimized
  Register Level Access
  Small code expressions
  Closely follows the reference manual
  Debugging close to register level
Limitations:
  Specific to STM32 devices, not portable directly between series
  Not matching complex peripherals such as USB
  Lack of abstraction means developers must understand peripheral operation at register level
  Available (today) on STM32 L0 and F0 series

## Slide 18: Standard Peripheral Libraries (SPL)
Portability | Optimization (Memory & Mips) | Easy | Readiness | Hardware coverage
++ | ++ | + | ++ | +++
What is it ?
  Collection of C Libraries covering STM32 peripherals
Target Audience
  Embedded systems developers with procedural C background. All existing STM32 customer base prior to the STM32Cube launch, willing to keep same supporting technology for future projects, and same STM32 series.
Features:
  Average optimization, fitting lots of situations
  No need for direct register manipulation
  100% coverage of all peripherals
  Easier debugging of procedural code
  Extensions for complex middleware such as USB/TCP-IP/Graphics/Touch Sense
Limitations:
  Specific to certain STM32 series.
  No common HAL API prevents application portability between series
  Middleware libraries may not be unified for each series
  Doesn’t support forward STM32 series starting with STM32 L0 and F7

## Slide 19: STM32Cube - Embedded software
STM32Cube
STM32 Hardware abstraction layer
STM32Cube
Middleware
User code
Portability | Optimization (Memory & Mips) | Easy | Readiness | Hardware coverage
+++ | + | ++ | +++ | +++
What is it ?
  Full featured packages with drivers, USB, TCP/IP, Graphics, File system and RTOS
  Set of common application programming interfaces, ensuring high portability inside whole STM32 family
Target Audience
  Embedded system developers with a strong structured C background. New customers looking for a fast way to evaluate STM32 and easy portability
Limitations:
  May be challenging to low level C programmers in the embedded space.
  Higher portability creates bigger software footprints or more time spent executing adaptation code
  Not Available (today) on STM32 F1 series
Features:
  High level and functional abstraction
  Easy port from one series to another
  100% coverage of all peripherals
  Integrates complex middleware such as USB/TCP-IP/Graphics/Touch Sense/RTOS
  Can work with STM32CubeMX tool on the PC to generate initialization code

## Slide 20: ST Embedded software offer – Comparison
Offer | Portability | Optimization (Memory & Mips) | Easy | Readiness | Hardware coverage
STM32Snippets |  | +++ |  |  | +
Standard Peripheral Library | ++ | ++ | + | ++ | +++
STM32Cube | +++ | + | ++ | +++ | +++

## Slide 21: ST Embedded software offer - Positioning
STM32Snippets
Standard Peripheral Libraries
STM32 Device
-specific
f.i.: STM32F072
STM32 Series
-specific
f.i.: STM32F1
STM32 Family
Portability Level
STM32Cube HAL
(Hardware Abstraction Layer)
TCP/IP
FAT
File
Sys.
Gfx
USB
Host / Device
STM32Cube Middleware level
RTOS
STM32Cube Embedded Software packages
Touch
Abstraction Level
TCP/IP
FAT
File
Sys.
Gfx
USB
Host / Device
RTOS
Touch
Libraries, released independently

## Slide 22: Availability
Offer | Available for STM32 |  |  |  |  |  |  |  | 
STM32Snippets | Now | N.A. | N.A. | N.A. | N.A. | N.A. | Now | N.A. | N.A.
Standard Peripheral Library | Now | Now | Now | Now | Now | N.A. | N.A. | Now | N.A.
STM32Cube | Now | Now | Now | Now | Now | June 15 | Now | Now | Sept 15

## Slide 23: STM32Cube Ecosystem

## Slide 24: STM32CubeTM Introduction
STM32CubeTM includes:
  A configuration tool, STM32CubeMX generating initialization code from user choices
  Firmware offering, delivered per series (like STM32CubeF4) with:
    An STM32 Abstraction Layer embedded software: STM32Cube HAL
    A consistent set of Middleware: RTOS, USB, TCP/IP, Graphics, …
STM32Cube HAL: Portable API within all series - Middleware stacks when applicable: RTOS, USB, TCP/IP, Graphics, …
STM32CubeMX
STM32CubeF3
STM32CubeF2
STM32CubeF4
STM32CubeF1
STM32CubeF0
STM32CubeL1
Initialization Code generation based on user choices
24
STM32CubeL0

## Slide 25
Pinout Wizard
Clock Tree wizard
Peripherals & Middleware
Wizard
Power Consumption
Wizard
STM32CubeMX
25

## Slide 26
STM32CubeMX
Generates Initialization C Code
based on user choices !
26

## Slide 27: STM32CubeMX: MCU Selector
Filter by:
Series
Line
Package
Peripherals

## Slide 28: STM32CubeMX: Pin-out configuration
Pinout from:
  Peripheral tree
  Manually
Automatic signal remapping
Management of dependencies between peripherals

## Slide 29: STM32CubeMX: Clock tree
Immediate display of all clock values
Management of all clock constraints
Highlight of errors

## Slide 30: STM32CubeMX: Peripheral configuration
Global view of used peripherals and middleware
Highlight of configuration errors
Manage:
  GPIO
  Interrupts
  DMA

## Slide 31: Power consumption calculator
Power step definitions
Battery selection
Creation of consumption graph
Display of
  Average consumption
  Average DMIPS
  Battery lifetime

## Slide 32: STM32Cube Supporting all STM32 MCUs
Generate your configuration code with the STM32Cube and you can focus on your added-value software !
  4 configuration wizards: pinout, clock, peripherals & middleware, power consumption
  Portable Hardware Abstraction layer, from series to others
  Middleware with RTOS, USB, TCP/IP, File System, Graphics , Touch sensing…
www.st.com/stm32cube

## Slide 33: STM32 ST-LINK Utility

## Slide 34: STM32 ST-LINK Utility
Standalone software tool allows in-system programming of STM32 devices
  Supports Binary, Hex and Motorola S-Record file formats
Allows programming option bytes
Supports ST-LINK/V2
Command line version available for usage with batch files and small quantity production
  ST-LINK_CLI.exe
  Supports multiple ST-LINK/V2 connected to same PC
User manual UM0892

## Slide 35: ST Visual Programmer

## Slide 36: STVP
Free software that supports Motorola S19 and Intel HEX formats
Load, Edit and Save executable and/or data files generated by the Assembler/Linker or C compilers
Erase, Program, View and Verify device Flash memory contents
Project mode to automate all configuration and programming tasks
Programming Toolkit with C/C++ source files for creating a programming application based STVP
STVP supports microcontroller programming via a complete range of hardware development tools and dedicated programmers, including:
  ST-LINK in-circuit debugger/programmer for STM8 and STM32

## Slide 37: STM32 FLASH LOADER DEMONSTRATOR

## Slide 38: FLASH LOADER DEMONSTRATOR
Illustrate the System Memory boot loader capabilities
The Flash loader demonstrator is designed to work with all STMicroelectronics devices that support the system memory boot mode UART protocol

## Slide 39: DFUSE

## Slide 40: DFUSE
Perform the upgrade operation with some requires, such as:
  Product identifier
  Vendor identifier
  Firmware version
  Alternate setting number (Target ID) of the target to be used,
These information makes the upgrade targeted and more secure.
To add this information, a new file format should be used, to be called DFU file format

## Slide 41: STMSTUDIO

## Slide 42: STMSTUDIO
STM Studio is a non-intrusive tool, preserving the real-time behavior of applications.
STM Studio perfectly complements traditional debugging tools to fine tune applications.
It is well suited for debugging applications which cannot be stopped, such as motor control applications.
Connects to any STM32 via ST-LINK (JTAG or SWD protocols), reads on-the-fly (non intrusive) variables from RAM while application is running

## Slide 43: FOC SDK

## Slide 44: STMSTUDIO
ST’s STM32 offers the performance of the industry-standard Cortex®-M core at the service of vector (or field-oriented) control (FOC) algorithms, widely used in high-performance drives.
The STM32 PMSM FOC SDK (STSW-STM32100), which includes the PMSM FOC FW library and ST MC Workbench, allows the user to evaluate the STM32 performance in applications driving single or dual Field Oriented

## Slide 45: free SW licensing program
Unleashing the power of embedded software with algorithms and complete demonstrators for the Internet of Things.
Bring your ideas to now!
Notes: This presentation will introduce the open.Audio free software licensing program.
Open.Audio is part of the ST Open Software Expansion initiative (OSX).
The Open Software Expansion (OSX) development suite offers drivers, middleware and application software to jump start your STM32 design with ST products like MEMS, Bluetooth low energy, environmental sensors, etc. It enables fast prototyping using the STM32 Open Development Environment with leading-edge components that can quickly be transformed into final designs.
The Open Software Expansion environment is made up of several free libraries:
• Open.MEMS: sensor fusion library for STM32 platform
• Open.RF: BlueNRG Bluetooth low energy library for the most commonly used BT smart profiles
• Open.Audio: embedded audio libraries and application software
It also includes implementation examples in the Open.Framework section. The BlueMicrosystem1 expansion software package uses a Bluetooth low energy (BlueNRG) network processor for communication and includes complete middleware to build applications using pressure, temperature and humidity sensors as well as motion sensors (MEMS).
Start your design today with our Open Software Expansion development suite.

## Slide 46: STM32 ODE Nucleo and X-Nucleo
Move / actuate
Connect
Power
Sense
Process
Inertial modules, magnetometer
Proximity, microphone
Pressure, temperature, humidity, UV
Bluetooth LE, Sub-GHz radio
NFC, Wi-Fi, GNSS
Energy management & battery
General purpose microcontrollers
Stepper motor driver
DC & BLDC motor driver
Audio amplifier
DATA COLLECT
DATA TRANSMIT
DATA ACCESS
DATA CREATE
DATA POWER
DATA PROCESS
Software
Secure microcontrollers
Touch controller
Operation Amplifier
Accelerometer, gyroscope
Translate
STM32 Nucleo
Nucleo Expansion Boards
The building blocks
Your need
Our answer

## Slide 47: STM32 M0 Overview
Cortex Architecture Overview
ARM Cortex Interrupt Overview
Debug System Overview

## Slide 48: ARM Cortex-M0 Architecture Overview

## Slide 49: STM32 Cortex-M0 implementation
Cortex-M0 components
Cortex-M0 processor
Nested Vectored Interrupt Controller (NVIC)
Cortex-M0 processor core
BUS MATRIX
DEBUG
Breakpoint Unit (BPU)
+
Data Watchpoint Trigger (DWT)
Debugger Interface
Debug Access Port (DAP)
AHB-Lite interface to system
Serial Wire Debug (SWD)
IRQs
3-stage pipeline
(1)
SLEEP
SysTick
Timer

## Slide 50: Memory map overview
4GB linear memory space
No paging/banking
All locations always accessible by the SW
Supports 8/16/32-bit data
Standard across all Cortex-M implementations
0x00000000
0xFFFFFFFF
CODE region
SRAM region
0x20000000
0x40000000
Peripheral region
RAM region
Device region
0x60000000
0xA0000000
System region
0xE0000000
Program flash
SRAM
Peripherals
Off chip memory
Off chip peripherals
System components
and debug
(XN)
(XN)
(XN)
Notes: 50
Straight forward memory map

## Slide 51: Core Registers
All registers are 32-bit wide
  Instructions exist to efficiently support packed 8/16/32-bit data in memory
13 general purpose registers
  Registers r0 – r7 (Low registers)
  Registers r8 – r12 (High registers)
Only 3 special registers (MRS, MSR)
  Stack Pointer (SP) – r13
  Link Register (LR) – r14
  Program Counter (PC) – r15
Program Status Register
  (Application / Interrupt / Execution)
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (PC)
r14 (LR)
PSR
r13 (SP)
Notes:   The same as ARM7TDMI and all other ARM processors
  Instructions exist to efficiently support packed 8/16/32-bit data in memory
R0-R7: Accessible to all instructions
Registers R8-R12 : Accessible to a few 16-bit / all 32-bit instructions
R13 is the stack pointer
R14 is the link register
R15 is the program counter
xPSR (Program Status Register)
  Not Explicitly accessible
  Saved to the stack on an exception
  Subsets available as APSR, IPSR
Two stack pointers – main stack pointer (used after reset and in exception handlers) and process stack pointer (can be used only in thread mode)

## Slide 52: Stack Pointer and Stacks
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (PC)
r14 (LR)
PSR
r13 (SP)
Process Stack Pointer
Main Stack Pointer
0
1
CONTROL register
31
0
1
2
Active stack pointer
Only in Thread Mode !
RTOS

## Slide 53: Processor modes
THUMB STATE
DEBUG STATE
LOCKUP STATE
Thread Mode
Normal code execution
Exception return
Exception request
RESET
STATE
Debug
operations
Handler Mode
Exception handler execution
Exception request
Process Stack
/
Main Stack
(default)
Main Stack

## Slide 54: Exception Model – States
Inactive
  NOT Pending/Active
Pending
  Waiting to be serviced by the processor
  On Interrupt request generated by a peripheral or from software
Active
  Actually serviced exception state
  More exceptions can be active at a time
Active and pending
  Exception is being serviced, but another request from the same source came already

## Slide 55: ARM Cortex Interrupt Overview

## Slide 56: Exception Model – Types and Priorities
No. | Exception Type | Priority | Type of Priority | Descriptions
1 | Reset | -3 (Highest) | fixed | Reset
2 | NMI | -2 | fixed | Non-Maskable Interrupt
3 | Hard Fault | -1 | fixed | Default fault if other handler is not implemented
4-10 | Reserved | N.A. | N.A. | 
11 | SVCall | Programmable | settable | Supervisor call (SVC)
12-13 | Reserved | N.A. | N.A. | 
14 | PendSV | Programmable | settable | Request for System-Level Service
15 | SYSTICK | Programmable | settable | System Tick Timer
16 | Interrupt #0 | Programmable | settable | External Interrupt #0
…… | ………………….. | ……………….. | settable | …………………..
47 | Interrupt#31 | Programmable | settable | External Interrupt #31
4 priority levels
Notes: On ARM-v7M MemManage, UsageFault and BusFault exceptions with
support for escalation to HardFault.
2 priority bits

## Slide 57: Interrupt Entry and Return
Interrupt handling is micro-coded
→ No instruction overhead
Entry (“Stacking”)
  Processor state automatically saved to the stack over the bus
    {PC, xPSR, R0-R3, R12, LR}
    What about the other registers?
  Then, ISR ready to start executing as soon as stack PUSH complete
Exit (“Unstacking”)
  Processor state is automatically restored from the stack
  Then interrupted instruction is executed upon completion of stack POP
Notes: - The Interrupt Service Routine (ISR) generally must:
  - Clear the interrupt source (in peripheral)
  - Do the required interrupt work
  - Return from interrupt

## Slide 58: Preemption
“Interruption of the exception handler”
Depending on the priority
If higher priority exception request comes while another lower priority exception handler is executing
→ the higher priority exception can preempt the lower priority exception handler
Such exceptions are called nested exceptions

## Slide 59: Exception Response
Standard exception latency is 16-cycles
  The latency from processor clock cycle time when the exception is asserted to the first instruction of the exception handler execution
  0 memory wait states
Can be reduced by the following two mechanisms:
  Tail Chaining
  If exception request exists or occurs just as another exception handler returns
      → Stacking process can be skipped
  Late arriving (Late arrival)
  If higher priority exception request occurs during lower priority exception stacking process
      → Higher priority exception handler is called right after the stacking finishes

## Slide 60: Interrupt Response – Tail-Chaining
PUSH
POP
ISR 1
PUSH
POP
ISR 2
PUSH
ISR 1
POP
ISR 2
26
16
26
16
16
IRQ1
IRQ2
ARM7
Interrupt handling in assembler code
Cortex-M0
Interrupt handling in HW
16
42 CYCLES
Highest
Tail-chaining
ARM7
26 cycles from IRQ1 to ISR1 entered
  Up to 42 cycles if LSM
42 cycles from ISR1 exit to ISR2 entry
16 cycles to return from ISR2
Cortex-M0
16 cycles from IRQ1 to ISR1 entered
6 cycles from ISR1 exit to ISR2 entry
16 cycles to return from ISR2
Saving in Clock Cycles
6
Notes: Tail-chaining is back-to-back processing of exceptions without the overhead of state
saving and restoration between interrupts. The processor skips the pop of eight registers
and push of eight registers when exiting one ISR and entering another because this has
no effect on the stack contents.
The processor tail-chains if a pending interrupt has higher priority than all stacked
exceptions.
On cortex-M3 the push takes only 12 cycles because we have I and S bus than can be pushed fetched on same time
Here 12 cycles for context saving, then 4 cycles for reading the vector table…

## Slide 61: Interrupt Response – Late Arriving
ISR 2
IRQ1
IRQ2
ISR 2
Tail-Chaining
ISR 1
PUSH
PUSH
POP
POP
PUSH
POP
ARM7
Cortex-M0
Highest
Cortex-M0
Stack push to ISR 2 is interrupted
Stacking continues but new vector address
is fetched in parallel
Late-arrival to ISR1 entry will depend
of the PUSH status, then 4 cycles
will be necessary to read the vector table.
Tail-chain into ISR 2
ARM7
26 cycles to ISR2 entered
Immediately pre-empted by IRQ1 and
takes a further 26 cycles to enter ISR 1.
ISR 1 completes and then takes 16
cycles to return to ISR 2.
26
16
16
26
16
6
ISR 1
16

## Slide 62: NVIC – Vector Table
Vector Table starts at location 0
  In the code section of the memory map
Vector Table contains addresses (vectors)
of exception handlers and ISRs
  Not instructions
Table size (in words) is = number of IRQ inputs + 16
  Minimum size ( case of 1 IRQ) : 17 words
  Maximum size ( case of 32 IRQs) 48 words
Main stack pointer initial value in location 0
  Set up by hardware during Reset
Vector Table can not be relocated
  The vector table is always seen at address 0x00000000,
  Different Boot option or memory remap function, allow user to alias at this direction, SRAM, FLASH or System Memory
Address | Vector
0x00 | Initial Main SP
0x04 | Reset
0x08 | NMI
0x0C | Hard Fault
0x10-0x28 | Reserved
0x2C | SVCall
0x30-0x34 | Reserved
0x38 | PendSV
0x3C | Systick
40 | IRQ0
… | More IRQs
Notes: Vector Table Offset Register (VTOR) is not available on Cortex-M0; It is available on Cortex-M0+, M3 and M4. It allows you to dynamically relocate vector table, and is useful for implementing bootloaders and also for running interrupt code from RAM during Flash Write/Erase without any stall on devices that do not have dual-bank Read-While-Write capability.

## Slide 63: Debug System Overview

## Slide 64: Debug subsystem
Breakpoint Unit (BPU)
  Instruction Comparison
Data Watchpoint (DWT)
  Data Comparison
Debug Access Port (DAP)
  Background access to all memory and registers
  Interface to outside debug host via SWD
M0 Core
BUS
BPU
DWT
DAP
Cortex-M0
ROM
SRAM
Peripherals
DBGMCU

## Slide 65: Debug – Main features
Break on instruction fetch (PC comparison) or data access data match
Serial Wire interface (SWD), only two pins!
Break point unit (BPU) – 4 breakpoints
  Core is stopped on a given instruction fetch
Data watchpoint trigger (DWT) – 2 watchpoints
  data address and PC sampling
Additional DBGMCU peripheral:
  low-power modes
  timers, watchdog and I2C behavior during breakpoint
  device ID code
SWDIO
SWCLK
VDD
VSS
Note: on STM32F0x2 devices, SWDIO pull-up is connected to VDDIO2

## Slide 66: Debug – Device ID detection
2 registers which can be used to check device type and also its unique ID
MCU device ID code (DBGMCU):
Unique device ID register (UID)
  96-bit register
  X,Y coordinates on the wafer + Lot number + Wafer number
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Revision ID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Division ID |  |  |  | Device ID |  |  |  |  |  |  |  |  |  |  | 
Revision of the device
ST division (0x6)
0x440
Notes: Note: 96-bit Unique ID is not available in Value Line devices (STM32F0x0)

## Slide 67: Architecture & Peripherals

## Slide 68: System Architecture
Multiply possibilities of bus accesses to SRAM, Flash, Peripherals, DMA
  BusMatrix added to allow parallel access
Efficient DMA and Rapid data flow
  Direct path to SRAM through arbiter, guarantees alternating access
  Von Neumann + BusMatrix allows Flash execution in parallel with DMA transfer
Increase Peripherals Speed for better performance
  Advanced Peripheral bus (APB) architecture up to 48MHz
   Allows to optimize use of peripherals (18MBits/s SPI, 6Mbps USART, 48MHz GP-Timer, 12MHz toggling I/Os)
BusMatrix
System
CORTEX-M0
Master 1
GP-DMA
Master 2
SRAM
Slave 1
FLASH
Flash I/F
Slave 3
AHB2APB
AHB
Slave 2 Bridges
APB
Arbiter
SYSCFG, TIMs, WWD, IWWD, RTC,
I2Cs, USARTs, SPI/I2Ss, HDMI-CEC,
BxCAN, USB, DBGMCU
RCC, CRC, Touch
Sensing controller (TSC)
Buses are not overloaded
with data movement tasks
DMA
AHB2GPIO
GPIO A, B ,C, D, E, F
AHB
AHB
AHB
Slave 4 Bridge
Notes: Several AHB subsystems
Dedicated AHB to GPIO
Each peripheral can be reset independently on APB

## Slide 69: Boot Modes
BOOT Mode Selection |  |  |  | Boot Mode | Aliasing
nBOOT1 bit | BOOT0 pin | BOOT_SEL bit | nBOOT0 bit |  | 
X | 0 | 1 | X | User Flash | User Flash is selected as boot space
1 | 1 | 1 | X | System memory | System Memory is selected as boot space
0 | 1 | 1 | X | Embedded SRAM | Embedded SRAM is selected as boot space
X | X | 0 | 1 | User Flash | User Flash is selected as boot space
1 | X | 0 | 0 | System memory | System Memory is selected as boot space
0 | X | 0 | 0 | Embedded SRAM | Embedded SRAM is selected as boot space
Boot modes
  Depending on the Boot configuration, Embedded Flash memory, System memory or Embedded SRAM memory
  is aliased at @0x00. Even when aliased, these memories are still accessible from their original memory space.
The boot configuration is defined with BOOT0 pin, nBOOT1 bit, nBOOT0 bit and BOOT_SEL bit from USER option byte.
System memory : contains the Bootloader used to re-program the FLASH through USART1 (same pins configuration as for STM32 products).
  Boot from SRAM : The relocation of the vector table is not allowed on the Cortex M0. When Booting from SRAM, System memory or User Flash, the vector table will be aliased at direction 0x00000000
69
Notes: Field in blue are availables on STM32F04x only. The boot pin can be disabled through Option bits, offering an additional GPIO for users.
Notes: The bytes are treated in memory as being in Little Endian format.
Even when aliased in the boot memory space, the related memory (FLASH or SRAM) is still accessible at its original memory space.
- Only 12 bytes (6 + 6 complemented) are used as option bytes
System memory: contains the Boot Loader is used to re-program the FLASH through the USART.
The Boot Loader is programmed by ST during production.
RAM remapping feature is particularly useful for managing Reset vectors and routines, you can copy them to SRAM, modify and access them even when Flash is not available (i.e. during Flash programming or erasing).
-Parity check
The data bus width is 36 bits because 4 bits are available for parity check (1 bit per byte) in
order to increase memory robustness, as required for instance by Class B or SIL norms.
The parity bits are computed and stored when writing into the SRAM. Then, they are
automatically checked when reading. If one bit fails, an NMI is generated. The same error
can also be linked to the BRK_IN Break input of TIMER1, with the SRAM_PARITY_LOCK
control bit in the SYSCFG configuration register 2 (SYSCFG_CFGR2). The SRAM Parity
Error flag (SRAM_PEF) is available in the SYSCFG configuration register 2
(SYSCFG_CFGR2).

## Slide 70: Flash Read Protection (FLASH)
Level 2 RDP=0xCC
Level 0 RDP=0xAA
Level 1
RDP ≠ 0xCC
RDP ≠ 0xAA
SWD fuse
SWD disabled, System memory disabled
User settings protected
No un-protection possible → IRREVERSIBLE!!!
Full access to memory from SRAM, system memory and SWD
No readout protection
BLOCKED access to memory from SRAM, system memory and SWD
Remove of readout protection still possible after full erase of the memory and its blank verification

## Slide 71: Flash Protections (6/6)
Area | Protection level | User execution |  |  | Debug, boot from RAM or boot from system memory (loader) |  | 
 |  | Read | Write | Erase | Read | Write | Erase
Main memory | 1 | Yes | Yes | Yes | No | No | No
 | 2 | Yes | Yes | Yes | N/A | N/A | N/A
System memory | 1 | Yes | No | No | Yes | No | No
 | 2 | Yes | No | No | N/A | N/A | N/A
Option bytes | 1 | Yes | Yes | Yes | Yes | Yes | Yes
 | 2 | Yes | Yes | No | N/A | N/A | N/A
Backup registers | 1 | Yes | Yes | N/A | No | No | N/A
 | 2 | Yes | Yes | N/A | N/A | N/A | N/A
Access status versus protection level and execution modes :
Notes: Option byte in user mode level 2 : cannot be erase and RDP cannot be programmed.
Yellow yes lvl1: The main flash memory is erased when the RDP option byte is programmed with all levels protection disabled
Yellow yes lvl2: All option bytes can be programmed, except the RDP byte

## Slide 72: Power Supply
VSS
VDD
VBAT
VDDA
VSSA
VDDA domain
LSE crystal 32K osc
BKP registers
RCC BDCR register
RTC
Backup domain
Core
Memories
Digital
peripherals
V18 domain
VDD domain
STANDBY circuitry
(IWDG, RTC, LSE
crystal 32K osc,
RCC CSR )
Voltage Regulator
VDDIO1 I/O Rings
Low Voltage Detector
Power Supply Schemes
  VDD = 2.0 to 3.6 V: External Power Supply for I/Os and the internal regulator.
    On STM32F0x8 (regulator off part), VDD = 1.8V(+/- 8%): An external regulator must be used.
  VDDA = 2.0 to 3.6 V: External Analog Power supplies for ADC,DAC, Reset blocks, RCs and PLL.
     ADC or DAC working only if VDDA >=2.4V
  VDDIO2 = 1.65V to 3.6V: External Power Supply for some GPIOs which then have a flexible voltage versus the VDD, and Power supply for the USB Transceiver.
  VBAT = 1.65V to 3.6 V: For Backup domain when VDD is not present.
  Power pins connection:
    VDD and VDDA can be provided by a separated power supply source.
    VSS and VSSA must be tight to ground
Note: The voltage regulator (outlined in blue on the scheme) is not present on the STM32F0x8 products.
VDDIO2
VSS
VDDIO2 domain
VDDIO2 I/O Rings
USB Tranceiver
A/D converter
D/A converter
COMP
Temp. sensor
Reset block
PLL

## Slide 73: POR, PDR Circuitry (PWR)
Two Integrated POR / PDR circuitries guarantees proper product reset when voltage is not in the product guaranteed voltage range (2V to 3.6V)
  No need for external reset circuit
POR and PDR have a typical hysteresis of 40mV
The external power supply VDDIO2 can also be monitored. A comparator is embedded between its voltage and the Vrefint, triggering an external interrupt if its drop below this voltage.
VDD and VDDA
POR
PDR
40mv hysteresis
Reset
Vtrh
Vtrl
Tempo 2.5ms
Vtrl min 1.8V / Vtrh max 2V

## Slide 74: PVD Circuitry (PWR)
Programmable Voltage Detector
  Enabled by software
  Monitor the VDD power supply by comparing it to a threshold
  Threshold configurable from 2.1V to 2.9V by step of 90mV
  Generate interrupt through EXTI Line16 (if enabled) when VDD < Threshold and/or VDD > Threshold
   Can be used to generate a warning message and/or put the MCU into a safe state
VDD
100mv hysteresis
PVD
Output
PVD Threshold

## Slide 75: RTC Domain (PWR)
RTC Domain contains
  Low power calendar RTC (Alarm, periodic wakeup from Stop/Standby)
  20 Bytes Data RTC registers
  Separate 32kHz Osc (LSE) for RTC
  RCC BCSR register: RTC clock source selection and enable + LSE config
   Reset only by RTC domain RESET
VBAT independent voltage supply
  Automatic switch-over to VBAT when VDD goes lower than PDR level
  No current sunk on VBAT when VDD present
Auto-wakeup feature on STM32F07x devices.
Tamper event detection: resets all user backup registers
TimeStamp event detection.
Backup Domain
32KHz OSC
(LSE)
RTC + 20 Bytes Data
RCC BDSR
reg
Wakeup
Logic
IWWDG
VBAT
VDD
power switch
RTC_TAMPx

## Slide 76: Reset and Clock Control (RCC)
System Clock (SYSCLK) sources:
  HSE (High Speed External osc) 4MHz to 32MHz, can be bypassed by user clock
  HSI (High Speed Internal RC): factory trimmed internal RC oscillator 8MHz +/- 1%
  HSI48 (High Speed 48 MHz RC): In application trimmed through CRS. F04/7 only
  internal PLL x2, x3, .. x16 (16MHz min. output freq.)
Additional clock sources:
  LSI (Low Speed Internal RC): ~40kHz internal RC
  LSE (Low Speed External oscillator): 32.768kHz, can be bypassed by user clock
    configurable driving strength (power/robustness compromise)
  HSI14 (High Speed Internal RC 14MHz): dedicated oscillator for ADC
Clock-out capability on the MCO for all sources.
Clock Security System (CSS) to switch to backup clock in case of HSE clock failure & Clock Recovery System to monitor the 48MHz oscillator
RTC Clock sources: LSE, LSI and HSE clock divided by 32
USART, I2C & CEC have multiple possible clock sources

## Slide 77: RESET Sources
System RESET
  Resets all registers except some RCC registers and Backup domain
  Sources
    Low level on the NRST pin (External Reset)
    WWDG end of count condition
    IWWDG end of count condition
    A software reset (through NVIC)
    Low power management reset
    Option byte loader reset (FORCE_OBL bit)
Power RESET
  Resets all registers except the Backup domain
  Sources
    Power On/Power down Reset (POR/PDR)
    Exit from STANDBY
Backup domain RESET
  Resets in the Backup domain: RTC registers + Backup Registers + RCC_BDCR register
  Sources
    BDRST bit in RCC_BDCR register
    POWER Reset
Filter
VDD
RPU
PULSE
GENERATOR
(min 20µs)
SYSTEM RESET
NRST
WWDG RESET
IWWDG RESET
Software RESET
Power RESET
Low power management RESET
External RESET
Standby exit
POR/PDR
Option byte loader RESET
Notes:   New:
  pullup control
  Option byte loader reset

## Slide 78: DMA Features
5 independently configurable channels (requests)
4 levels of priority settable by software consisting of very high, high, medium, low
Independent source and destination transfer size (byte, half word, word)
Support for circular buffer management
3 event flags (DMA Half Transfer, DMA Transfer complete and DMA Transfer Error)
Peripheral-to-memory, memory-to-peripheral, peripheral-to-peripheral & Memory-to-memory transfers
Access to Flash, SRAM, APB and AHB peripherals as source and destination
Programmable number of data to be transferred: up to 65536 (16-bit counter)

## Slide 79: DMA Latency: 1 transfer
Request1 sample & arbitration phase
Bus access
Address computation
Acknowledgement phase
1 cycle
1 cycle
2 cycles
1 cycle
Request 1
5 cycles for each request in better case
(source and destination on AHB with the CPU not running)
Request2 sample & arbitration phase
Request 2
Then different parameters can impact the bus access and add delay cycles to the default value:
If the CPU is running | If source or destination is an APB Peripheral, it introduce a bridge latency. |  | If CPU is competing with DMA to access the APB Peripheral. (AHB frequency bigger than APB)
 | AHB and APB are same frequency | APB frequency is the half of AHB frequency | 
+ 2 cycles | +3 cycles | +5-6 cycles | +4 cycles

## Slide 80: DMA Latency: 2 transfers
To improve the DMA performances, a new request can be served while the previous one is running : if a request is active and other ones are pending, the new request sample & arbitration phase is performed during AHB bus access of the current request. The winning request AHB bus access will start immediately after the end of the current request‘s AHB Bus access.
  if source or destination is on APB, the transfer will take more cycles (+ 2 cycles for APB:AHB = 1:1)
HCLK
Ch. 1
Request sample & arb. phase
Addr. computation
Ch. 2
Bus access
Bus access
Ack. phase
Bus access
Request sample & arb. phase
Addr. computation
Ack. phase
Request sample & arb. phase
Addr. computation

## Slide 81: DMA and Bus occupation
Request, arbitration and acknowledgement operations are done outside AHB system bus, so the bus is not occupied during those phases
One DMA access takes 2 cycles (on AHB): if the
CPU is running the system Bus
can not be totally freeze by DMA as at least
2 cycles are left to the CPU
during one DMA transaction.
Current DMA controller compared to others which permit burst transfer have nearly the same system bus occupation rate. However, it doesn’t freeze the bus for many cycles consecutively as it is the case with the burst mode: better performance with many small data transfer without blocking the bus
Read
Write
Read
Write
Bus access
Bus access
Those Idle states are only present when CPU are conflicting on the AHB Bus with DMA.
AHB Control
AHB Data
Bus free for CPU

## Slide 82: Watchdogs (IWDG / WWDG)
Window Watchdog (WWDG)
  Configurable Time Window
  Can detect abnormally early or late application behavior
  Conditional Reset
  WWDG Reset flag
  Timeout value @48MHz: 85.33us … 43.69ms
Independent Watchdog (IWDG) → IWWDG
  Dedicated low speed clock (LSI)
  IWDG clock still active if main clock fails
  HW and SW way of enabling
  Still functional in Stop/Standby
  Wake-up from stop/standby
  IWDG Reset flag
  Window Functionality
  Timeout values @40KHz (LSI): 100us …26.2s
Notes: TODO: timeout graficky

## Slide 83: WWDG features
CMP
W0
W1
W2
W3
W4
W5
W6
-
T0
T1
T2
T3
T4
T5
T6
WDGA
WWDG_CR
WWDG_CFR
PRESCALER
(WDGTB)
6-Bit Down Counter
PCLK
(up to 48MHz)
Write WWDG_CR
comparator
= 1 when
T6:0 > W6:0
WWDG Reset
Configurable time-window, can be programmed to detect abnormally late or early application behavior
Conditional reset
  Reset (if watchdog activated) when the down counter value becomes less than 40h (T6=0)
  Reset (if watchdog activated) if the down counter is reloaded outside the time-window
To prevent WWDG reset: write T[6:0] bits (with T6 equal to 1) at regular intervals while the counter value is lower than the time-window value (W[6:0])
Early Wakeup Interrupt (EWI): occurs whenever the counter reaches 40h  can be used to reload the down counter
WWDG reset flag (in RCC_CSR) to inform when a WWDG reset occurs
Min-max timeout value @48MHz (PCLK): 85.33μs / 43.69ms
Best suited to applications which require the watchdog to react within an accurate timing window
Refresh
not allowed
Refresh
Window
T[6:0] CNT down counter
time
W[6:0]
3Fh
T6 bit
Reset
Notes: If the watchdog is activated (the WDGA bit is set in the WWDG_CR register) and when the 7-bit down counter (T[6:0] bits) rolls over from 40h to 3Fh (T6 becomes cleared), it generates a
reset. If the software reloads the counter while the counter is greater than the value stored in the window register, then a reset is generated.
WWDG Counter can be stopped when the core is halted, If enabled in the DBG module.

## Slide 84: IWDG features
Selectable HW/SW start through option byte
Advanced security features:
  IWDG clocked by its own dedicated low-speed clock (LSI) and thus stays active even if the main clock fails
  Once enabled the IWDG can’t be disabled (LSI can’t be disabled too)
  Safe Reload Sequence (key) + window
  IWDG function implemented in the VDD voltage domain that is still functional in STOP and STANDBY mode (IWDG reset can wake-up from STANDBY)
To prevent IWDG reset: write IWDG_KR with AAAAh key value at regular intervals before the counter reaches 0, while respecting the defined refresh window
IWDG reset flag (in RCC_CSR) to inform when a IWDG reset occurs
Min-max timeout value @40KHz (LSI): 100μs / 26.2s
Best suited to applications which require the watchdog to run as a totally independent process outside the main application
8-bit
PRESCALER
LSI
(40KHz)
12-bit
reload value
Prescaler
Register
Status
Register
Reload
Register
Key
Register
IWDG Reset
VDD voltage domain
1.8V voltage domain
Window
Register
12-bit
window comp
12-bit
down counter
Notes: When the independent watchdog is started by writing the value CCCCh in the Key Register (IWDG_KR), the counter starts counting down from the reset value of FFFh.
When it reaches the end of count value (000h) a reset signal is generated (IWDG RESET).
Whenever the key value AAAAh is written in the IWDG_KR register, the IWDG_RLR value is re-loaded in the counter and the watchdog reset is prevented.
If the “Hardware watchdog” feature is enabled through the device option bits, the watchdog is automatically enabled at power on, and will generate a reset unless the
Key register is written by the software before the counter reaches end of count.
IWDG Counter can be stopped when the core is halted, If enabled in the DBG module.

## Slide 85: EXTI Features
Manages the external and internal asynchronous events/interrupts and generates the event request to the CPU/Interrupt Controller and a wake-up request to the Power Manager
Some communication peripherals (UART, I2C, CEC, comparators) are able to generate events when the system is in run/sleep mode and also when the system is in stop mode allowing to wake up the system from stop mode.
These peripherals are able to generate both a synchronized (to the system APB clock) and an asynchronous version of the event.
All others features are same as STM32F1x series
Up to 28 Interrupt/Events requests :
  Up to 55 GPIOs can be used as EXTI line(0..15)
  EXTI line 16 is connected to the PVD output
  EXTI line 17 is connected to the RTC Alarm event
  EXTI line 18 is reserved (internally held low)
  EXTI line 19 is connected to RTC tamper and Timestamps
  EXTI line 20 is reserved (internally held low)
  EXTI line 21 is connected to Comparator 1 output
  EXTI line 22 is connected to Comparator 2 output
  EXTI line 23 is connected to I2C1 wakeup
  EXTI line 24 is reserved (internally held low)
  EXTI line 25 is connected to USART1 wakeup
  EXTI line 26 is reserved (internally held low)
  EXTI line 27 is connected to CEC wakeup.
EXTI[15:0]
Interrupt Mask
Register
Pending Request
Register
Software Interrupt
Event Register
Rising Trigger
Selection Register
To NVIC
Edge Detect
Circuit
Pulse
Generator
Falling Trigger
Selection Register
Event Mask
Register

## Slide 86: GPIO features
Up to 55 multifunction bi-directional I/O ports available on biggest package 64 pin. ( 86% ratio versus 80% STM32F1 series)
Almost all standard I/Os are 5V tolerant (ADC pins are not)
All Standard I/Os are shared in 5 ports: GPIOA [0..15], GPIOB[0..15], GPIOC[0..15], GPIOD[2], GPIOF[0,1,4..7]
Atomic Bit Set and Bit Reset using BSRR and BRR registers
GPIO connected to AHB bus: max toggling frequency 12 MHz
Configurable Output slew rate speed up to 50MHz
Locking mechanism (GPIOx_LCKR) provided to freeze the I/O configuration on ports A and B
Up to 55 GPIOs can be set-up as external interrupt (up to 16 lines at time) able to wake-up the MCU from low power modes
86
Notes: 55 I/Os on 64pin package
55 I/Os on 64pin package

## Slide 87: General-Purpose I/Os (GPIO)
OUTPUT | Push-Pull
 | Open drain (Pull-up, Pull-down)
INPUT | Floating (Pull-up, Pull-down)
 | Analog
2MHz
10MHz
50MHz
...................
.....
TO / FROM
PERIPHERALS
PIN
EMC
NO CONFLICTS
ADC / DAC
TSC
IDR
ODR
BSRR
up to 16
standard / 5V tolerant
ESD
(5VT)
FLEXIBILITY
Fast toggle capable of changing every two clock cycles
Locking mechanism provided to freeze the port I/O configuration
Bitwise write access
GPIO READ / WRITE
25mA max
Notes: MULTIPLEXERS -> (no conflicts on the pin)
FLEXIBILITY -> several pin configuration options
EMC -> selective transition time and ESD protection
Highly flexible pin multiplexing allows the use of I/O pins as GPIOs or as one of several peripheral functions
IDR = Input Data Register
ODR = Output Data Register
BSRR = Bit Set Reset Register
TSC = Touch Sensing Controller

## Slide 88: GPIO Configuration Modes
(1) VDD_FT is a potential specific to five-volt tolerant I/Os and different from VDD.
To On-chip Peripherals
Analog
From On-chip Peripherals
Push-Pull
Open Drain
Output Driver
I/O pin
VSS
On/Off
Pull - Up
Pull - Down
VDD
On/Off
Bit Set/Reset
Register
Input Data Register
Output Data Register
Read / Write
Alternate Function Input
Alternate Function Output
Schmitt
Trigger
VDD
VSS
0
Input Driver
Read
Write
On
Off
VDD or VDD_FT(1)
VSS
OUTPUT
CONTROL
Analog
MODER(i)
[1:0]
OTYPER(i)
[1:0]
I/O configuration
PUPDR(i)
[1:0]
11
x
Analog mode
x
01
0
0 0 Output Open Drain
0 1 Output Open Drain with Pull-up
1 0 Output Open Drain with Pull-down
1
0 0 Output Push Pull
0 1 Output Push Pull with Pull-up
1 0 Output Push Pull with Pull-down
10
0
1
0 0 Alternate Function Open Drain
0 1 Alternate Function OD Pull-up
1 0 Alternate Function OD Pull-down
0 0 Alternate Function Push Pull
0 1 Alternate Function PP Pull-up
1 0 Alternate Function PP Pull-down
00
x
0 0 Input floating
0 1 Input with Pull-up
1 0 Input with Pull-down
* In output mode, the I/O speed is configurable through OSPEEDR register: 2MHz, 10MHz or 50MHz
88

## Slide 89: Alternate Functions features
Most of the peripherals shares the same pin (like USARTx_TX, TIMx_CH2, I2Cx_SCL, SPIx_MISO, EVENTOUT…)
Alternate functions multiplexers prevent to have several peripheral’s function pin to be connected to a specific I/O at a time. Available only for Port A and Port B
Some Alternate function pins are remapped to give the possibility to optimize the number of peripherals used in parallel.
AF0 (SPI1_MISO)
AF1 (TIM3_CH1)
AF2 (TIM1_BKIN)
AF7 (COMP1_OUT)
Pin x (0…7)
89

## Slide 90: Atomic operations - BSRR and BRR
Very often we need fast and atomic access to GPIO pins
To avoid any read + modify + write access
Multiple bit modification at the same time in one operation
Write only
90
BR15
BR0
BS15
BS0
Write 1 means bit RESET in the ODR
Write 1 means bit SET in the ODR
With a correct combination you may set and reset any number of pins at the same time (one CPU write)
All other pins (where 0 was written) remain unchanged.
Notes: Don’t need to disable interrupts! Better latency for RT systems.

## Slide 91: Hands-On: Black Box to LED Blink in Five Easy Steps!

## Slide 92: Board Check
Connect USB ST-LINK (CN1, middle USB) to your PC
  ST-LINK driver may get installed if this is your first time with this board.
LD2 and LD3 one GREEN one RED

## Slide 93: Run STM32CubeMX

## Slide 94: Step 1: Create New Project
Create New Project
Select STM32F072RBTx
  LQFP64, 128kB Flash
Click “OK”
2
3
1

## Slide 95: Step 2: Pin Configuration
In this example we are going to use one of the LEDs present on the STM32F072 NUCLEO board.
Left-click PA5

## Slide 96: Step 3: Generate Source Code
Open Project > Settings (Alt + P)
Set the project name (Lab1) and the project location (C:\STM32CubeSeminar\Labs)
Set the IDE Toolchain to MDK-ARM V5
Click OK
Generate Code (Ctrl + Shift + G)
Click Open Project
2
3
1

## Slide 97: Step 4: Toggle The LED
The MDK-ARM IDE should now be open.
Expand the file tree and open the main.c file
Add the following code inside the while(1) loop
  Line 86 in “main.c”
HAL_GPIO_TogglePin(GPIOA, GPIO_PIN_5);
HAL_Delay(100);

## Slide 98: Step 5: Build the Project
Click the “Build” button; or use menu Project > Build target.
Click the “Start/Stop Debug Session” button (CTRL + F5)
Click the “Run” button (F5)
Enjoy the flashing LED!

## Slide 99: Oops

## Slide 100: Step 6(if needed): Configure STLink
Click the “Build” button; or use menu Project > Build target.
Click the “Debug” button and then Settings
Select the STLINK/V2 and the download checkbox